## Slide 1
Advanced Image Analysis
2017-2018, 2nd semester
Intensity transformations
Alessandro Bria
Contract Professor
and Post-doc Researcher
email: a.bria@unicas.it

## Slide 2: Intensity transformations
also called point-processing
simple to implement
  algorithms, functions, look-up-tables
used to enhance images that are devoted to visual processing
  no general rule for stating the optimality
  application/user-dependent
often designed based on the properties of the image histogram
image negative

## Slide 3: Image histogram

## Slide 4: Histogram
a histogram represents the distribution of (graylevel) intensities in the image
  the most important basic tool for image processing
the histogram of an -valued image is a discrete function
  where is the number of pixels with intensity
  often it is preferable to consider the histogram normalized with respect to the number of pixels
  estimates the probability density of :

## Slide 5: An example of histogram computation
image
graylevels
histogram

## Slide 6: Dark image
the histogram components are localized to low intensity values

## Slide 7: Bright image
the histogram components are localized to high intensity values

## Slide 8: Low contrast image
the histogram components are localized in a narrow region of the intensity values

## Slide 9: High contrast image
the histogram components are distributed over all the intensity range
  this is the effect pursued by the histogram based intensity transformations

## Slide 10: Contrast Enhancement

## Slide 11: Contrast enhancement
use a pointwise transformation to generate a new image from a given image such that
properties that must satisfy
  monotonically non-decreasing, so that relative brightness of pixels do not change
  bit depth preserving, i.e. has the same bitdepth of
  integer (rounding/truncation may be needed)
different possibilities
  linear functions
  piece-wise linear functions
  non-linear functions
  histogram equalization

## Slide 12: Linear stretching
enhances the dynamic range by linearly stretching the original gray levels
if the original graylevels are in and the target graylevels are , then
example
  the original graylevels are in
  the target graylevels are in
in this case we refer to the linear stretching transformation as image normalization

## Slide 13: Linear stretching

## Slide 14: Piecewise linear stretching
segments for input and output
for

## Slide 15: Piecewise linear stretching with
segment I
  slope
  input intensities are compressed in the output
segment II
  slope
  input intensities are stretched in the output
segment III
  slope
  input intensities are compressed in the output
points and can be determined using percentiles (e.g. 5% and 95%) of the input image histogram
  th percentile smallest
I
II
III
I
II
III

## Slide 16: Piecewise linear stretching (special case)
intensity level slicing
  highlights an intensity range
  both transformations in (a) and (b) set the intensities in to a high value
  the transformation in (a) sets all the intensities that are not in to a low value
  the transformation in (b) preserves the intensities that are not in
(a)
(b)

## Slide 17: Piecewise linear stretching (special case)
intensity level slicing
  highlights an intensity range
  both transformations in (a) and (b) set the intensities in to a high value
  the transformation in (a) sets all the intensities that are not in to a low value
  the transformation in (b) preserves the intensities that are not in
(a)
(b)

## Slide 18: Logarithmic transformations
nonlinear
  in order to preserve the original intensity range
useful to enhance dark images
  low intensity ranges are expanded
  high intensity ranges are compressed

## Slide 19: Logarithmic transformations (example)
original
log-transformed

## Slide 20: Gamma transformations
also called power-law transformations
  in order to preserve the original intensity range
used to correct the visualization devices output
  thus the naming "gamma correction"
a too large or too small value for can compromise the results
  identity
  brightening
  darkening

## Slide 21: Gamma transformations (brightening)
original image
gamma-transformed with
gamma-transformed with
gamma-transformed with

## Slide 22: Gamma transformations (darkening)
original image
gamma-transformed with
gamma-transformed with
gamma-transformed with

## Slide 23: Exercise
implement in C++/OpenCV all contrast enhancement techniques viewed so far and apply them on a low-contrasted image
  design a basic UI with trackbars to set parameters
  also display the image histogram using
    cv::Mat ucas::imhist(const cv::Mat & image)
  a low-contrasted image can be found at
std::string(EXAMPLE_IMAGES_PATH) + "/lowcontrast.png"
solution in /exercises/nonlinear-ui.cpp
solution in /exercises/linear-stretching-ui.cpp

## Slide 24: Histogram Equalization

## Slide 25: Definition
goal: given the p.d.f. of an input image , we want to apply an intensity transformation such that the output image has uniform p.d.f.
solution: solve for in the continuous domain () and then obtain the discrete approximation
input
desired output
solution
?

## Slide 26: Cumulative Distribution Function
the cumulative distribution function has an interesting property:
  is steeper where is more probable
  this results in mapping intervals of values with low probability into narrow intervals of
  on the contrary, intervals of values with high probability are mapped into large intervals of

## Slide 27: Solution
goal: given the p.d.f. of an input image , we want to apply an intensity transformation such that the output image has uniform p.d.f.
solution: use (the term preserves the intensity range)
input
desired output
solution

## Slide 28: Proof (for the continuous case)
Proof:
  we want to verify that applying yields
  = probability that apply
  = probability that
  = apply to both sides + chain rule
  small trick: apply chain rule
  replace in the left member

## Slide 29: Discrete histogram equalization
the continuous histogram-equalizing transformation is:
the corresponding (approximated) discrete histogram-equalizing transformation is:
which substituting with the original histogram formulation yields:

## Slide 30: Example: dark image equalization

## Slide 31: Example: bright image equalization

## Slide 32: Example: low contrast image equalization

## Slide 33: Example: high contrast image equalization

## Slide 34: Examples
the transformation of each image maps values from the range of the original images to the whole range of intensity levels
the transformation for (4) is close to the identity

## Slide 35: Should HE be always applied?
of course, no
  if the image has a bimodal-like histogram, equalization may worsen the contrast
    this is the case of dark/bright objects on homogeneous bright/dark background
original
equalized

## Slide 36: Adaptive Histogram Equalization (AHE)
histogram equalization based on a histogram obtained from a portion of the image
  preserves and enhances local properties
e.g. using a tiling approach
  subdivide into overlapping regions
  apply histogram equalization within each tile
  mitigate blocking effect by smooth blending between neighboring tiles
contrast limited AHE (CLAHE)
  limit contrast expansion in flat regions of the image by clipping histogram values

## Slide 37: Examples
original
HE
CLAHE

## Slide 38: Examples
original
HE
CLAHE

## Slide 39: Exercise
implement in C++/OpenCV both global and adaptive histogram equalization and apply them on a low-contrasted image
  design a basic UI with trackbars to set parameters
  also display the image histogram using
    cv::Mat ucas::imhist(const cv::Mat & image)
  a low-contrasted image can be found at
std::string(EXAMPLE_IMAGES_PATH) + "/lowcontrast.png"
solution in /exercises/histogram-equalization-ui.cpp